## Slide 1: Lathe Flow Diagram
Isolate power
Make sure lathe is clean and ready for use
Choose correct tool and fix in place securely
Get material and fix securely into chuck using chuck key
Centre the tool with the material held in chuck
Un isolate power
Face off material manually
Move tool away from material before stopping. Continue until at desired thickness
Set speed and touch surface of material with tool
Take material out of chuck
Set tool to 0mm then adjust to 1mm
Start machine turning material, 1mm at a time.
Isolate power
Find and mark the centre of material
Place material back into chuck
Set drill as close to chuck and material as possible.
make sure the brake is on.
Un isolate power
Drill whole in material slowly, do not force it quickly and use in and out motion
Isolate power
Remove material, and clean lathe completely